HB63B09M Prerelease Programmers Reference

© D. Collins – 2024

Intro and Forward:

The HB63C09M was an idea I hatched back two years ago when I was finishing up my first homebrew computer the HB6809. But it goes back further than that the beginning is really around 2020 when I started building kit computers as a means to pass the time durring the pandemic. I had purchased a kit from McJohn in Italy called the Z80-MBC2, by Fabio Defabis – an exelent little computer kit with a single logic chip, atmega32, Z80 CPU and a RAM chip. I was hooked on the small form factor and the things that I could do with my little computer. I made a few hardware expansions for it, most notibly a joystick interface for my tetris clone that I had programed in pascal. At the time there were people asking Fabio on the facebook group for the project if he was going to do other processors. Before long he was working on the V20-MBC (which I built) at the time and later went on to make the 68K-MBC which is architecturally slightly different. After a while, no new MBC computers were made, and by then I was on to building my 6809 based system, and still quite a novice at this (I am still!)

Things happened life got busy I spent some time working on other projects and about a year ago started playing around with arduino – and digging very deeply into the Z80-MBC2. I really wanted to understand how memory was loaded using a microcontroller and I wanted to know how Fabio had shared the bus with the Z80. At that time I had also stumbled onto an even older work, Brad Rodreguez’s “Scroungemaster” and I fell in love. The scroungemaster is (well was) a consept for a 6809 multi-processing build Brad had built on wirewrap. He had used a rather simple (but flawed for his design, perfect for mine turns out) circuit to do clock stretching in order to hand off cleanly to the other CPU’s into common ram. He detaled this in a paper entitled “Multiprocessing for the Impoverished” (found at https://www.bradrodriguez.com/papers/) I quitetly started to play around with the design and build a small expansion for the HB6809 that allowed me to use an arduino like a paripheral without a latch simply by stretching the clock.

In his paper, Brad discusses the paralells between the Z80 and the 6809. I found a lot of paralells in my arduino sketch and the work that Fabio had done with the Z80-MBC2, and after a few months I had a working prototype that could stage itself from the arduino (all beit with latches) and boot into a machine language monitor. After that I streamlined the design, making it slightly more like the Z80-MBC2’s little brother the Z80-MBC by opening up a few address lines to the arduino and then additionally solving a very difficult timing problem by changing from a generated clock to a synchrous clock (both the 63C09’s internal clock and the ATMEGA32 are clocked by the same 20Mhz crystal)

After a few revisons of the board, I found I could further srink the form factor to a smaller 10x10 PCB – albit 4 layers. The Exact same size PCB as the Z80-MBC2! For me, it was like coming full circle and now I think I am ready to share this design with others. What I have is a mostly finished – ready to go 63C09 playground. But theres still some work, this is where you come in.

What I am calling this board revision is “The Prerelease” edtion. This is basically all the hardware in a fixed what I am calling “finnished” state. The computer is ready to go, there is preconfigured and pre existing ported software and certainly enough for any homebrew enthusiast to be very excited about. What does not exist yet is ports for more advanced operating systems like FLEX, and OS9 (and its variants). The existing software is not patched to support the LBA images from the SD cards but thats the next thing on my list unless somebody beats me to it.

Section 1 – Architecture Overview

The chip set is designed to be as simple as possible, and so this introduces a few gotchas which we will go over here. The main chip besides the 63C09 CPU is the Atmega32 (hereafter referred to as the IO Controller), this is supported by seven other off the shelf logic chips. The data port on the IO controller is buffered by a bus transceiver to assure the controller is off the bus at the appropriate time. There is an external bank register and buffer which handle the banking, along with a few decoder chips, buffers, logic gates and inverters. These together create what is called the “Bella” chip set. This 7 chip set is planed to be condensed into a single CPLD / GAL chip for miniaturization which will be called “Isabella”.

Clock stretching via MRDY:
 All IO exchanges introduce a clock stretch asserted by the MRDY signal. This means that any memory read or write to A000-AFFF (see table a below) will stretch the clock for a time. The length of time depends on how long the IO controller needs to complete the requested task. As of this edition, specific timing of each IO operation is not fully documented, in the next edition a full timing diagram will be made available. For the time being its best to assume that the wait state is never longer than the data sheet maximum (5uS) though some are considerably faster (such as a mezzanine read / write). The IO controller releases the clock stretch with an ~IO_Grant signal which originates at a pin on the IO controller.

Halt / Reset / DMA:
The Halt signal, and the Reset signals are open collector inputs on the CPU which will be pull different signals to tri-state when asserted through buffers within the chip set. Both signals have a pull up resistor which pulls their state to high if nothing is pulling them low (typically the IO controller).

When system reset is asserted, the MRDY line will be forced high by its pull up as it is cut off by the tri-state buffer when the active low reset pin is low. This effectively inhibits bus requests during reset and prevents logic on the mezzanine from causing an IO request during reset. Also keep in mind that the IO controller resets the CPU during boot up. The switch for reset is not the same reset line as the CPU’s reset line. The Switch simply resets the IO controller which in turn resets the CPU. The Reset line which is available on the mezzanine is the CPU reset line, and will not reset the IO Controller.

When the halt signal is asserted, the ~BRD / ~BWR signals are tri-stated. While the CPU is in halt all of its busses (control, address and data ) are tri-state. Since the intel similar RD / WR signals are generated by the chip set these signals must also be sent to tri-state during halt so that whatever is halting the CPU can strobe operations into the ram via these signals. NOTE: the R//W line and E are connected to the input of a 2 to 4 decoder, which generate the unbuffered RD/WR signals, during a halt these unbuffered signals are not reliable but in no way interface with the RAM chip while the halt signal is asserted. This also means that driving the R//W signal from an expansion during halt has no effect on the RAM chip. Conversely, a DMA device will only be able to to use R//W to access the ram chip, and will have to synchronize these transfers the same way the CPU would using the E clock (which is still generated during DMA).

IO Operations carried out by the IO Controller (bus mastering):

The IO controller is an ATMEGA32 based AVR. It can act as a very limited bus master, as well as handle IO requests like a peripheral IC. During boot the IO Controller halts the CPU and holds reset in order to shut down any IO requests and tri-state the bus. While in this mode it has access to only the first 6 address lines A0-A5. Additionally, the address bus is tied high by strong pull ups which hold the bus at address FFFF. The CPU can use these address lines to write up to 63 bytes to the top of memory. This is just enough to load a small bootstrap program, as well as update the reset vector table. The first thing the computer does at boot up after asserting reset and halt is test to see if the SD card and RAM are available. Once the status of the system is verified the IO controller strobes a very short program at the top of memory that contains the 63C09 for loading data off of the memory card. After this is loaded, the controller is set up to accept commands as a peripheral, and the halt and reset states are lifted. Once lifted the 63C09 jumps to the reset vector (the beginning of the self staging code), and runs it.

The self staging code relocates itself to 4000 hex, this location was chosen because it is the beginning of the fixed block and should work reliably even if the bank register is not functional. The code changes a few bytes of it’s programming to point itself at the loader. After it is finished copying and self modifying, the 63C09 jumps to 4000 hex and starts loading the data from the card using the information from a few variables stored in the EEPROM of the controller, these variables are for start, size and name of the rom and are set with the vBIOS environment (refer to the section on vBios for operation here). As long as the uploaded code properly sets the new reset vector, the computer resets and should boot to the staged code at the end of the copying process. The controller ultimately tracks the PC along with the CPU and sends the reset once the code is done coping. This is obviously a general overview of the self staging process. Please refer to the Sketch code comments as well as the source code for the loader for specifics into how the loader works. Additional information about the limitations of the loader can be found in the section on vBIOS.

IO Operations carried out by the IO Controller (peripheral):

In addition to staging the ram for boot up, the controller can also act as a Motorola type peripheral IC. Once the system has booted in 63C09 Mode the IO controller takes on a more traditional roll. It offers the ability to customize in software. At this time by modifying the Arduino sketch, however mini device drivers are planned. This will allow the 63C09 side of the computer to load code AVR into the EEPROM, which the controller will be able to integrate into the system on boot up for things like custom I2C devices and more – this may take some time to build as there are other priorities such as new hardware expansions for off board IO, video and keyboard etc…

To access the IO controller the programmer has to simply write to, or read from a memory mapped device IO address. A handful of options are set up at the moment but more are being thought of and added as time allows. Since we’ve reached what I consider a architectural milestone – there should be an expectation that nothing in the IO range should move or be changed in the main source fork without a community backed decision. So early development should not need excessive patching to resolve firmware updates.

Below is table a1 and a2 containing a breakdown of the available programmed IO which can be used currently:

tables on next page

WRITE OPERATIONS:
ADDRESS	NAME	DESCRIPTION
0xA000	NULL	Legacy 6850 UART Control register. May use later (future use)
0xA001	TXSERIAL	6850 Wrapper: Send a byte to TX Buffer (default buffer size is 64bytes)
0xA002	SELDISK*	Select Disk Number ie: 0..99
0xA003	SELTRACK*	Select Disk Track ie: 0..511 (two bytes in sequence)
0xA004	SELSECT*	Select Disk Sector ie: 0..31
0xA005	WRITESECT*	Write a Sector to the Disk (512 bytes in sequence)
0xA006		Reserved for Immediate core use, requires community feedback
…		Reserved for Immediate core use, requires community feedback
0xA00F		Reserved for Immediate core use, requires community feedback
0xA010		Reserved for device drivers not implemented, requires community feedback
…		Reserved for device drivers not implemented, requires community feedback
0xA01F		Reserved for device drivers not implemented, requires community feedback
0xA020		Free space for DIY and experimentation, core code should not reference this
…		Free space for DIY and experimentation, core code should not reference this
0xA02F		Free space for DIY and experimentation, core code should not reference this
0xA030		Registers, Stored values operational space, requires community feedback
…		Registers, Stored values operational space, requires community feedback
0xA03E	LOADERR	This is the loader register it is unlocked by writing 255 after boot up.
0xA03F	SETBANK	Write the low nibble (3 bits) on the data bus to the bank register

Figure a1

READ OPERATIONS:
ADDRESS	NAME	DESCRIPTION
0xA000	UARTSTAT	6850 Wrapper: simulates a 6850 Status register, see appendix a for details
0xA001	RXSERIAL	6850 Wrapper: Read a byte from the RX buffer (default buffer size is 64bytes)
0xA002	ERRDISK*	Read out the last disk error
0xA003	READSECT*	Read a sector from the disk (512 bytes in sequence)
0xA004	SDMOUNT*	Mount the installed volume (output error code as read value)
0xA006		Reserved for Immediate core use, requires community feedback
…		Reserved for Immediate core use, requires community feedback
0xA00F		Reserved for Immediate core use, requires community feedback
0xA010		Reserved for device drivers not implemented, requires community feedback
…		Reserved for device drivers not implemented, requires community feedback
0xA01F		Reserved for device drivers not implemented, requires community feedback
0xA020		Free space DIY and experimentation, core code should not reference this
…		Free space for DIY and experimentation, core code should not reference this
0xA02F		Free space for DIY and experimentation, core code should not reference this
0xA030		Registers, Stored values operational space, requires community feedback
…		Registers, Stored values operational space, requires community feedback
0xA03E	LOADER	This is the loader port its typically locked to the user.
0xA03F	RDBANK	Read the last selected bank value

Figure a2

* - These functions imported / ported from the Z80-MBC2 project by Fabio Defabis, an open source GPL licensed project. Please see attribution in repository, thank you Fabio.

Expansion Connector (Mezzanine connection):

 The Mezzanine connector pin out (Figure 1) shows the pin out configuration for the large expansion connector on the edge of the board. The expansion connection has no specific address decoding within the chip set on the main single board computer, instead – the expansion needs to provide at the point of connection:

- Buffers for bus and address connections.
- Address decoding within the range of 0xA040 and 0xAFFF.
- An active low, open collector request signal to !XSIN on the expansion header.

Figure 1

The !XSIN signal being brought low via an open collector output will trigger the controller to ignore any io request for the current cycle, as well as block the controller transceiver from enabling on the SBC. At relatively the same time that the request comes in, the controller should see the IO request is from the Mezzanine and pass the grant signal along to the clock stretching circuit. This tiny wait state is not measured as of yet but should be by the next release of the document. For the time being please use the cpu address bus decay as the end of the cycle for driving the data bus, by driving your bus transceiver enable line to your address decode logic.
Remember – even though expansions are connected to the bus, the IO controller still needs to grant access to the mezzanine before the clock can continue. Additionally – any IO request within the range of A000 and AFFF will trigger an IO request.

The 74ALS156 is an example of a suitable decoder chip for driving !XSIN, another practical solution would be to use a single gate in a 74AHC125, following traditional push / pull logic by connecting the enable pin of the gate to the output, connecting the gate’s input to ground and connecting the output to the !XSIN signal. In this configuration the output of the gate will ether be high Z (when the enable pin is high) or Low (when the enable pin is low). Caution connecting push pull logic to this pin could damage the inverter which drives the IO request logic.

Keep in mind, you can also re-map internal IO Controller functions by decoding the same address and sending the !XSIN signal. For instance – you could over map the on circuit UART with another controller or video circuit for that matter. By setting up address decode logic to pick of A000 and A001. This allows an upgrade pathway for core features, an is an unintended “feature” of the simplicity of the architecture.

Open Collector Requirements:

Open collector logic is a way to allow multiple outputs to be connected to a single input, with less expense and hardware. However it does require you follow some rules when deciding on logic types you would like to use in a perspective enhancement or expansion. Below is a list of all of the CPU / IO Controller connected signals that require this attention to detail:

- !HALT
- !RESET
- !IRQ
- !DMA
- !XSIN

use of any of these pins from the mezzanine, requires an open collector output of some sort. Driving these inputs high – even for a short while could cause damage to these subsequent inputs. Please reference the perspective data-sheets for the HD63C09 and the ATMEGA32 on the requirements of these inputs as well. For the most part we have made reasonable accommodations, however there are some edge cases which require additional research in order to properly terminate links on any line.

I2C (work in progress) / SPI and UART:

I2C has been brought to the edge connector, however use of any device on the edge connector will require the software side to be configured inside the IO Controller sketch. I will work on an example case statement to show how this can properly be done using the wire library.

The SCL and SDA lines are tied high with 4.7k ohm pull up resistors which seemed like a good general purpose choice for the unterminated lines. Please keep this in mind when using I2C from the expansion and design your board to board connection appropriately.

SPI is exposed to the SD-Card interface, and to the ICSP port. As the HB63C09M uses the same architecture and circuit for SD cards as the Z80-MBC2 and others, you can not use both interfaces at the same time. This limitation was imposed to simplify the design.

UART is wired only to the Serial connection header, !DTR is wired to Atmega32 reset line, this is for eventual compatibility with Arduino boot loader – however the only way to program the Atmega at the moment is via ICSP.

Bank Register:

The bank register is how the computer knows which 16K page to expose to the bottom of the 64K memory map. The computer uses decode logic to determine if it should use the address bus transceiver or the bank register to drive the top most address lines on the 128K RAM chip. The value of the register is stored in two locations. Firstly on the register itself, which is clocked by the IO controller during the write operation as its inputs are on the bus. Second, it is saved internal to the IO Controller, so that the user is able to read out the last bank number that was latched into the register. Under normal circumstances these two numbers should be the same, but its important to keep in mind the IO Controller has no way to read out the bank address, in the event that there is an issue with the bank register or the address transceiver, as these two values are stored in two different locations. To set the bank page you write the bank number to memory location A03F. To read the last value written to the bank register read from memory location A03F. See table a1 and a2 for details.
Section 2 – Memory Map Overview

	ROM / RAM Configuration
Addreses	64K Main Address Space
C000-FFFF	Upper Fixed RAM 16K Legacy Physical ROM Space
B000-BFFF	Upper Fixed RAM 4K Expanded Legacy ROM Space
A000-AFFF	Device Address Space for MCU 4K
8000-9FFF	Lower Fixed 8K of Fixed Lower Ram Area *
4000-7FFF	Lower Fixed 16K of Fixed Lower Ram Area *
0000-3FFF	Memory Bank Window, set by bank register (16K) *

	128K RAM Chip Layout
1C000-1FFFF	Bank 7 (16K)
18000-1BFFF	Bank 6 (16K)
14000-17FFF	Bank 5 (16K)
10000-13FFF	Bank 4 (16K)
C000-FFFF	Bank 3 (16K) Upper Fixed RAM 16K Legacy Physical ROM Space
B000-BFFF	Bank 2 (4K) Fixed RAM Expanded ROM Space “Shadow” (3000-3FFF in bank)**
A000-AFFF	Bank 2 (4K) Bank 2 Free RAM Area “Behind” IO Space (2000-2FFF in bank)**
8000-9FFF	Bank 2 (8K) Lower Ram Area Top 8K “Shadow” (0000-1FFF in bank)**
4000-7FFF	Bank 1 (16K) Fixed Lower Ram Area Bottom 16K
0000-3FFF	Bank 0 (16K) bottom 16K of ram chip. Boots with this selected.

table b

* - when combined with the lower bank this totals 40K of contiguous memory
** - caution, there is shadowed ram in bank two between 0000-1FFF, and again in 3000-3FFF. Therefore the only “Usable Space” in bank 2 is 2000-2FFF These spaces are mapped again for clarity below:

Bank 2 Address Range	Description	128K Address Range
0000-1FFF	Lower Fixed RAM “Shadow” 8K	8000-9FFF
2000-2FFF	Usable Space 4K	A000-AFFF
3000-3FFF	Expanded ROM “Shadow” 4K	B000-BFFF

table c

On boot up the system resets the bank register, which selects bank 0. With this bank selected in a traditional 64K layout the system has access to 40K before the IO range (see table b), and 20K after the IO Range. All of these areas are RAM and can be written to as the ROM is loaded to RAM from SD card on boot up. Bank 2 overlaps both the Fixed memory areas (table c), a programmer should be careful to not accidentally overwrite data in these two locations as there are no safeguards within the very minimal chip set to prevent this from happening.

Accessing the IO range will initiate an IO request within the chip set. This causes the E strobe to stop for a time through the assertion of the MRDY signal. The IO controller will read or write from the bus and return control to the internal clock by sending a !IO_GRANT. This happens for ALL IO requests including any requests from the mezzanine connection, however in this case the IO controller releases the bus quickly as possible, however there is some small wait state when reading or writing to expansions. Exact lengths of all the wait states are still being determined, though many are less than a few micro-seconds, within the next release - full timing diagrams should be available for the IO controller. Please see the architecture overview for a complete listing of internal commands handled by the IO Controller.
Section 3 – vCMOS Staging environment

The Staging environment is loaded by pressing <esc> when directed during a 3 second pause on boot up. This loads a very minimal dos like environment for setting the staging environment settings. Typing SHOW will bring up the list of system variables that can by set by the vBIOS environment:

Each command assists in the setting of the environment variables: START, SIZE, FILE and PATH.

The START variable contains the start address for the loader.

The SIZE variable is how many bytes to be loaded before resetting the CPU.

The FILE variable is what file to load within the selected PATH. vBIOS can only load a single file starting at a specific address. This file should ideally load to the end of memory so that it can overwrite the reset vector as the last operation the IO Controller performs is a reset to boot the system.

The PATH variable is the name of the directory to use when loading the environment. This variable is also used by iOS to determine where to load file system images from for any given system ROM

Continues on next page

These variables are set by the specific commands which are inside the vBIOS Environment. You can type HELP <ENTER> or simply ‘?’ <ENTER> to bring up the list of commands:

CD – switches directories within the root of the SD card, vBIOS supports switching to directories off the root, but not subdirectories. This is a limitation of how petitFS library works combined with wanting to keep the vBIOS environment as lean as possible. Additionally, vBIOS has no way of deleting or removing files from FAT due to the same limitations. – this is not a limitation of iOS however, as this uses file system images which can be manipulated exactly like a LBA device.

COMMIT – places the variable changes into the EEPROM inside the IO controller to be recalled at boot up.

DIR – brings up a list of all the files in the currently selected directory. Keep in mind it will list subdirectories if they exist but due to the way that path storage works, CD can only select directories off the root of the SD card.

HELP – Simply brings up the on line help message, the same result happens by sending the ? Character as well.

QUIT – Exits and attempts to boot the staged changes.

SET – sets a variable to a value see the examples pictured above. This can be a string value or a hexadecimal number – due to the way SET works, do not make the name of the rom file a Hexadecimal number, as this will potentially confuse the selection logic. Additionally setting to a system rom contained in a subdirectory will also update the PATH variable to the given path. Also note that you can not currently specify a path and a file separated by /. You must set the file and the path separately (or alternatively update FILE while in a subdirectory, which sets PATH). And update those values with COMMIT to change them.

SHOW – Shows the currently set variables used by boot up, keep in mind these variables still need to be saved to EEPROM with COMMIT if you wish to change what the computer uses at start up.

Limits of the loader:

The loader can only load files to ram which are contiguous. Additionally when the loader reaches the end of the file it resets the 63C09 CPU which causes a jump to the physical address stored at the reset vector. If the file loaded by the loader does not write a new reset vector, the computer will jump to whatever is stored there (by default this is the beginning of the bootstrap code which is at FFC0). If the loader bootstrap code was also not overwritten this will cause an infinite loop with the code loading to memory and the CPU never jumping to this location.

Another limitation is the Loader bootstrap code relocates itself to address 4000, so that the top of memory will be free for use by the loader, since typically most 6x09 roms load at the top of memory. Therefore any contiguous load that copies over the first 60 bytes or so starting from 4000 will also cause a crash to happen.

Lastly, the IO range starts at A000, and there is no way to tell the loader to skip a segment of memory, therefore the 64K pysical top addresses starting at B000 are realistically the only addresses that make sense, as the loader has to load contiguosly until it reaches the reset vector.

The best way to avoid these limits is to load the system to the top of the RAM, finishing at FFFF, doing so will guarantee that FFFE an FFFF are updated with something ( the address of the start of your system code should be stored there as it is the reset vector).

If further areas of ram need to be loaded during staging the best way to do this, is by loading enough rom space with the loader to interface with the iOS LBA interface, and loading the remaining data from the first LBA device image in the directory using a custom loader.

Further notes on iOS and how it interacts with system variables:

Once a ROM image is loaded with loader, the directory the rom is contained in becomes the location for that ROM’s LBA images. In other microcontroller based designs like the Z80-MBC2, different image naming was used to separate different environments, as all of the images were stored in the root of the SD card. With the HB63C09M, all of the system images follow the same naming convention for every instance: DS0NXX.DSK, where XX is any number between 0 and 99, however the image for the specific rom being loaded will be picked from the same directory the rom is loading from.

The LBA (logical block addressed) images must all be laied out as follows:

- 512 tracks (0-511), selected by a two byte write to SELTRACK in big endian format (see table a1)
- 32 sectors per track (0..31), selected by a 1 byte write to SELSECT (see table a1)
- 512 bytes per sector, which must be read into ram or written to sd consecutively, and completely (see appendix)

Therefore each LBA file must be 8,388,608 bytes exactly (regardless of any logical layout within
your operating system).